## Slide 1
Four phases, nine datasets
Sovereign Compute Nexus · Ceará case study · every layer joins one H3 grid
Boundaries
IBGE · MMA · FUNAI
Land cover + water
MapBiomas
1
Harmonize + exclude
2,808 cells
Sentinel-2 optical
Copernicus · GEE
Sentinel-1 radar
Copernicus · GEE
2
Degradation risk
Pdeg per cell
Policy corpus, 36 docs
Planalto · MME · MMA · law
Boundaries
2.5 km review buffer
3
Policy classifier
Low · Medium · Critical
Grid topology
ONS
Curtailment
ONS
Fiber anchors
PeeringDB · OSM
Plant inventory
GEM
4
Constrain + rank
819 → 448 → 25 sites
DATA
PHASE
OUTPUT
Facility inventory (110 sites) and the 27-state screen appear on the maps only. Explorer: giasmith.github.io/brazil-dc
Notes: Phase 1 harmonizes all layers onto 2,808 H3 resolution-8 cells and applies hard exclusions (conservation units, indigenous lands, surface water, outside state). Phase 2 derives the degradation probability from quarterly Sentinel-2 and Sentinel-1 composites. Phase 3 is a deterministic policy classifier built from the 36-document corpus; boundaries are reused for the 2.5 km human-review buffer. Phase 4 applies the operator constraints (HV bus within 25 km, line within 15 km, interconnection facility within 50 km) and sorts survivors on a six-objective Pareto frontier: 819 feasible, 448 on the frontier, 25 recommended.